## Slide 1: Detecting Peering Infrastructure Outages ENOG14, Minsk
Vasileios Giotsas †∗, Christoph Dietzel † §, Georgios Smaragdakis ‡ †, Anja Feldmann †, Arthur Berger ¶ ‡, Emile Aben #
†TU Berlin ∗CAIDA §DE-CIX ‡MIT ¶Akamai #RIPE NCC

## Slide 2: Peering Infrastructures are critical part of the interconnection ecosystem
Internet Exchange Points (IXPs) provide a shared switching fabric for layer-2 bilateral and multilateral peering.
Largest IXPs support > 100 K of peerings, > 5 Tbps peak traffic
Typical SLA 99.99% (~52 min. downtime/year)1
Carrier-neutral co-location facilities (CFs) provide infrastructure for physical co-location and cross-connect interconnections.
Largest facilities support > 170 K of interconnections
Typical SLA 99.999% (~5 min. downtime/year)2
1 https://ams-ix.net/services-pricing/service-level-agreement 2http://www.telehouse.net/london-colocation/
Notes: GEORGE: Maybe also mention the critical infrastructure nature of interconnections (DHS, EU)?
The physical topology matters
I would change it slightly -- CFs and IXPs are key enablers for this transition

## Slide 3: Outages in peering infrastructures can severely disrupt critical services and applications
Notes: I would use the term externalities here; effect to economy and users
Outages happend and when they do have severe implications

## Slide 4: Outages in peering infrastructures can severely disrupt critical services and applications
Outage detection crucial to improve situational awareness, risk assessment and transparency.

## Slide 5: Current practice: “Is anyone else having issues?”
ASes try to crowd-source the detection and localization of outages.
Inadequate transparency/responsiveness from infrastructure operators.
Notes: Although this is so important, the way we currently detect such outages is ad-hoc

## Slide 6: Our Research Goals
Outage detection:
  Timely, at the finest granularity possible
Outage localization:
  Distinguish cascading effects from outage source
Outage tracking:
  Determine duration, shifts in routing paths, geographic spread
Notes: In this work we aim to automate this process and provide hard evidence of what happened hopefully even provide forensics
Automated
Finest granularity
HARD evidence
Towards (future goal) to use for forensics
Active measurements incur large overhead, don’t scale well

## Slide 7: Passive outage detection: Initialization
For each vantage point (VP) collect all the stable BGP routes tagged with the communities of the target facility (Facility 2)
Time
Notes: GEORGE:: bottom of the Figure: animation of failure -- and how the links move elsewhere
In order to understand how this work in practice, let's take the example of the AMSIX outage.
Through a BGP listener we can find the number of paths that cross a specific facility or IXP for some time. For example here we can see 30K paths crossing AMS-IX through BGP communities.

## Slide 8: Passive outage detection: Initialization
For each vantage point (VP) collect all the stable BGP routes tagged with the communities of the target facility (Facility 2)
AS_PATH: 1 x
COMM: 1:FAC2
AS_PATH: 2 1 0
COMM: 2:FAC2
AS_PATH: 4 x
COMM: 4:FAC2
Time
Notes: GEORGE:: bottom of the Figure: animation of failure -- and how the links move elsewhere
In order to understand how this work in practice, let's take the example of the AMSIX outage.
Through a BGP listener we can find the number of paths that cross a specific facility or IXP for some time. For example here we can see 30K paths crossing AMS-IX through BGP communities.

## Slide 9: Passive outage detection: Monitoring
Track the BGP updates of the stable paths for changes in the communities values that indicate ingress point change.
Time
Notes: GEORGE:: bottom of the Figure: animation of failure -- and how the links move elsewhere
In order to understand how this work in practice, let's take the example of the AMSIX outage.
Through a BGP listener we can find the number of paths that cross a specific facility or IXP for some time. For example here we can see 30K paths crossing AMS-IX through BGP communities.

## Slide 10: Passive outage detection: Monitoring
AS_PATH: 2 1 0
COMM: 2:FAC1
We don’t care about AS-level path changes if the ingress-tagging communities remain the same.
Time
Notes: GEORGE:: bottom of the Figure: animation of failure -- and how the links move elsewhere
In order to understand how this work in practice, let's take the example of the AMSIX outage.
Through a BGP listener we can find the number of paths that cross a specific facility or IXP for some time. For example here we can see 30K paths crossing AMS-IX through BGP communities.

## Slide 11: Passive outage detection: Outage signal
AS_PATH: 2 1 0
COMM: 2:FAC1
AS_PATH: 1 x
COMM: 1:FAC1
AS_PATH: 4 x
COMM: 4:FAC4
4:IXP
Concurrent changes of communities values for the same facility.
Indication of outage but not final inference yet!
Time

## Slide 12: Passive outage detection: Outage signal
AS_PATH: 2 1 0
COMM: 2:FAC1
AS_PATH: 1 x
COMM: 1:FAC1
AS_PATH: 4 x
COMM: 4:FAC4
4:IXP
Concurrent changes of communities values for the same facility.
Indication of outage but not final inference yet!
Partial outage
Time

## Slide 13: Passive outage detection: Outage signal
AS_PATH: 2 1 0
COMM: 2:FAC1
AS_PATH: 1 x
COMM: 1:FAC1
AS_PATH: 4 x
COMM: 4:FAC4
4:IXP
Concurrent changes of communities values for the same facility.
Indication of outage but not final inference yet!
Partial outage?
De-peering of large ASes?
Major routing policy change?
Time
Notes: Necessary but not sufficient!

## Slide 14: Passive outage detection: Outage signal
AS_PATH: 2 1 0
COMM: 2:FAC1
AS_PATH: 1 x
COMM: 1:FAC1
AS_PATH: 4 x
COMM: 4:FAC4
4:IXP
Signal investigation:
Targeted active measurements.
How disjoint are the affected paths?
How many ASes and links have been affected?
Partial outage?
De-peering of large ASes?
Major routing policy change?
Time

## Slide 15: Passive outage detection: Outage tracking
AS_PATH: 1 x
COMM: 1:FAC2
AS_PATH: 2 1 0
COMM: 2:FAC2
End of outage inferred when the majority of paths return to the original facility.
Time

## Slide 16: De-noising of BGP routing activity
The aggregated activity of BGP messages (updates, withdrawals, states) provides no outage indication.
Time
Number of BGP messages (log)
105
103
101
Notes: -- Top: call it the off-the-shelf solution is prone to false alarms, e.g., there are peaks that are not related to any outage; can be e.g., peaks in announcements, related to BGP mirroring or re-announcements

## Slide 17: De-noising of BGP routing activity
The aggregated activity of BGP messages (updates, withdrawals, states) provides no outage indication.
The BGP activity filtered using communities provides strong outage signal.
Time
Number of BGP messages (log)
105
103
101
Time
Number of BGP messages (log)
105
103
101
1.0
0.4
0.2
0.6
0.8
Fraction of infrastructure paths
0
Notes: -- Top: call it the off-the-shelf solution is prone to false alarms, e.g., there are peaks that are not related to any outage; can be e.g., peaks in announcements, related to BGP mirroring or re-announcements

## Slide 18: Outage localization is more complicated!
The location of community values that trigger outage signals may not be the outage source!
Communities encode the ingress point closest to our VPs (near-end infrastructure)
  ASes may be interconnected over multiple intermediate infrastructures
  Failures in intermediate infrastructures may affect the near-end infrastructure paths

## Slide 19: Outage localization is more complicated!
Time

## Slide 20: Outage localization is more complicated!
Time

## Slide 21: Outage localization is more complicated!
Outage in Facility 2 causes drop in the paths of Facility 4!
Time

## Slide 22: Outage localization is more complicated!
Time

## Slide 23: Outage localization is more complicated!
Outage in Facility 3 causes drop in the paths of Facility 4!
Time

## Slide 24: Outage source disambiguation and localization
Create high-resolution co-location maps:
  AS to Facilities, AS to IXPs, IXPs to Facilities
  Sources: PeeringDB, DataCenterMap, operator websites
Decorrelate the behaviour of affected ASes based on their infrastructure colocation.
Notes: We localize the outage signal by studying the behaviour of each of the affected ASes in relationship to the infrastructures in which it is present, and we try correlate the behaviour of networks in the same infrastructures
Part of this work is to maintain an accurate colocation map. Tricky because networks are located in multiple sources

## Slide 25: Outage source disambiguation and localization
Paths not investigated in aggregated manner, but at the granularity of separate (AS, Facility) co-locations.
London Telecity HE8/9 outage
London Telehouse North outage
Time
Notes: The previous case of outage detection is a simple one because the location of the outage corresponds to the location encoded in the Communities that triggered the signal. However, the location encoded in the BGP communities of a signal may not correspond to the location of the outage. As we saw earlier, between two ASes there may be multiple intermediate facilities but the Communities tag only the nearest one. Therefore, when an intermediate facility fails the signal will be reflected on the nearest facility even if it’s not the outage source. For instance, consider this example which shows the number of paths that cross the Telehouse East facility.

## Slide 26: Outage source disambiguation and localization
London Telecity HE8/9 outage
London Telehouse North outage
London Telecity HE8/9 outage
London Telehouse North outage
Paths not investigated in aggregated manner, but at the granularity of separate (AS, Facility) co-locations.
Time
Notes: We can see which ASes are affected, and for how long. In many cases networks are affected by both cases.

## Slide 27: Tracking the progress of outages
Passive tracking: Monitor how location-tagging BGP Communities change during the outage.
Active tracking:
Execute targeted traceroutes based on the hints of the BGP signals.
Notes: On the top of each figure add the outage, AMS-IX and TC HEX8/9 and remove it from the text
-- Maybe you want to show the differences in the delays in the left figure; Do you want also to include figure 13a and 13b and have one slide for AMS-IX [you can include this figure after the AMS-IX outage discussion, i.e., after slide 34] and the next slide for the global effect of the outage
-- Names some of the locations in the right one, .e.g, Taiwan, etc.

## Slide 28: Detecting peering infrastructure outages in the wild
159 outages in 5 years of BGP data
  76% of the outages not reported in popular mailing lists/websites
Validation through status reports, direct feedback, social media
  90% accuracy, 93% precision (for trackable PoPs)
Notes: -- bottom figure: this refers to the facilities that had an outage and then you want to check if the outage lasted less than X.XXXX%

## Slide 29: Effect of outages on Service Level Agreements
~70% of failed facilities below 99.999% uptime
~50% of failed IXPs below 99.99% uptime
5% of failed infrastructures below 99.9% uptime!
Notes: -- bottom figure: this refers to the facilities that had an outage and then you want to check if the outage lasted less than X.XXXX%

## Slide 30: Measuring the impact of outages
> 56 % of the affected links in different country, > 20% in different continent!
Median RTT rises by > 100 ms for rerouted paths during AMS-IX outage.
Number of affected links (log)
105
103
101
CDF
1.0
0.4
0.2
0.6
0.8
0
0.44
Distance from outage source (km)
12K
8K
10K
6K
4K
0
2K
Fraction of paths
RTT (ms)
Notes: On the top of each figure add the outage, AMS-IX and TC HEX8/9 and remove it from the text
-- Maybe you want to show the differences in the delays in the left figure; Do you want also to include figure 13a and 13b and have one slide for AMS-IX [you can include this figure after the AMS-IX outage discussion, i.e., after slide 34] and the next slide for the global effect of the outage
-- Names some of the locations in the right one, .e.g, Taiwan, etc.

## Slide 31: Conclusions
Timely and accurate infrastructure-level outage detection through passive BGP monitoring
Majority of outages not (widely) reported
Remote peering and infrastructure interdependencies amplify the impact of local incidents
Hard evidence on outages can improve accountability, transparency and resilience strategies
Notes: -- Mention that you create a data base and a dashboard that policy makers, researchers, etc can explore. The insights can improve the design and operation of the internet.
In backup add the AMSIX/DECIX traffic interdependence

## Slide 32: Questions / Comments?

## Slide 33: Challenges in detecting infrastructure outages
Capturing the infrastructure-level hops between ASes
Correlating the paths from multiple vantage points
Continuous monitoring of the routing system
Before outage
During outage
During outage
VP
VP
No hop changes
The initial hops changed
Passive BGP monitoring

## Slide 34: Challenges in detecting infrastructure outages
Capturing the infrastructure-level hops between ASes
Correlating the paths from multiple vantage points
Continuous monitoring of the routing system
Before outage
During outage
During outage
VP
VP
No hop changes
The initial hops changed
Passive BGP monitoring
BGP encodes AS paths

## Slide 35: Deciphering location-metadata in BGP
BGP not entirely information-hiding!
Communities BGP attribute:
  Optional, tags BGP routes with arbitrary metadata
  Often encodes the ingress location of prefixes