## Slide 1: Role of Machine Learning in Network Monitoring and Automation
Cengiz Alaettinoglu

## Slide 2: Machine-Learning Analytics Empowers Network Automation
Application Services
Traffic Analytics
Performance
Analytics
Route Analytics
Traffic Engineering
MPLS VPNs
Multicast
JSON-based REST APIs
Latency, jitter, utilization and loss correlated with routing data for path-aware, service-aware performance analytics
Real-time monitoring of the network control plane and overlay services, forensic analysis and what-if modeling
IGPs, BGP-LS, BGP
MPLS L2 and L3 VPNs
RSVP-TE Tunnels & Segment Routing
Multicast
Flow records correlated with routing data for path-aware, service-aware traffic analytics
SDN Traffic Engineering
SDN Path Provisioning
Automated calculation and provisioning of TE tunnels to optimize traffic and relieve congestion
Automated provisioning of new service paths based on policy and network state
Notes: Intent: Provide an overview of the Explorer Suite, its components and high level architecture. Use this to align and describe the solution. Differentiate from other products with the fact that we see the network as the routers see it and we have real-time, historical, and future state/predictive analysis
Guidelines: Spend most time on the products/modules that align best with the client’s environment and goals you have discovered. If the client is unclear how Route Explorer works, you can use the next slide to explain. Don’t worry about network sizing and product licensing in the first meeting.
Asks: Ask use case questions so you can tailor the initial product demo to their problems/goals/needs.
The Packet Design Explorer Suite is comprised of the following products:
Route Explorer is the foundation for the product suite. It provides the control plane visibility and models on which traffic flow (Traffic Explorer) and SNMP performance metrics (Performance Explorer) are layered for path-aware service management.​
​
Open APIs enable customers to leverage Explorer Suite metrics and analytics in their own applications and portals and is the basis for the Packet Design SDN solution, including the two turn-key apps shown here. Customer investments in the Explorer Suite are future-proofed because the products are SDN-ready and can be leveraged to deliver custom applications for competitive differentiation. ​
​
An easy way to summarize the capabilities of the Explorer Suite is as follows:​
​
Past: With its “network DVR”, Network Engineers can play back routing events that occurred in the last few minutes, hours, days or weeks to solve transient, hard-to-find problems.​
​
Present: Real-time monitoring gives Operations teams visibility into routing and traffic health, and alerts them to errors and abnormal conditions (baseline threshold breaches) for immediate response. ​
​
Future: Unlike other planning tools (e.g. Riverbed Opnet, Cisco MATE, Juniper WANDL), Route Explorer maintains an always-current Layer 3 network model that can be used for highly accurate what-if analysis. Furthermore, modeling is interactive, not a laborious batch process requiring imported data and deep expertise. ​

## Slide 3: Network Automation Service Provider Trials
Provisioning assured bandwidth service paths
  No RSVP or SR tunnels
Provisioning service paths
  Various constraints
  Segment routing (SR-TE)
Proactive service restoration
  Link failure prediction
  Critical services are rerouted before failure
On-demand traffic engineering
  Multiple fiber cuts cause congestion and call drops
  On-demand tunnels are created for alleviating congestion
On-demand multi-layer traffic engineering
  Optimizing at the IP/MPLS layer alone still leaves some congestion
  New optical paths are signaled and LAGs are reconfigured to add capacity to the IP/MPLS layer

## Slide 4: Why Automate?
Medium-size service provider has 6% of its RSVP-TE tunnels down
  Due to race conditions after link failures
1200 down tunnels is too many for any operator to figure out the root cause
  If these tunnels are for traffic engineering, can we really say we are successfully doing traffic engineering?
  It is time for software/DevOps to manage the network?

## Slide 5: Machine Learning
Applications
  Autonomous driving, natural language processing, classification, recommender systems, anomaly detection, prediction, clustering, self-customization, database mining, handwriting recognition, …
Algorithms
  From simple linear regression to deep neural networks
  Neural networks are not new; however, access to large data sets and huge compute resources are now available and are responsible for recent attention
    Very popular in 1980s; stagnated until recently
It is not necessarily good at
  Magic – many algorithms require supervision
  Telling what it learned
  It is not always accurate; Siri doesn’t get me. I can’t even read my own handwriting…

## Slide 6: Machine Learning
Trends
  E.g. Detecting an optical interface card failure
Normal vs abnormal – anomaly detection
  BGP route hijacking
Clustering
  Subscriber behavior analysis
Recommender Systems
  Find similar past behaviors

## Slide 7: 1. Assured Bandwidth Service Paths
Service provider wants to offer a portal where customers can request assured bandwidth service paths
Can the network assure the service?
  Cannot disrupt current services; i.e. it cannot cause congestion
Shortest paths only
  No existing tunnels, nor plans to introduce tunnels

## Slide 8: Path Computation
Computing the shortest path is easy
Checking the interface utilizations along the shortest path is not sufficient
  What happens tonight when the traffic peaks?
    Or over the course of the week?
  What happens when a link fails?

## Slide 9: Role of Machine Learning
With nothing learned, all requests are accepted
  Very high probability of causing congestion for many requests
With just the real-time network demands and paths learned
  Very low probability of causing congestion in short term
  High probability of causing congestion later
With week-long network demands and paths are learned
  Very low probability of causing congestion now or later
Why stop at a week?
  Traffic has both diurnal and weekly patterns
  Networks evolve – new routers, new applications; better to forget at some point
Why not use neural networks here?

## Slide 10: 2. Intent Based Service Paths
Intent: provide subscribers paths with various service requirements
  Low-delay paths for financial enterprises
  Bandwidth-guaranteed paths for fat flows for broadcasters
  Diverse paths for full redundancy
  Geo-constrained paths for sensitive data
  “Pay what you use” on-demand, on-the-fly paths
Subscribers
  Cola, Pepsi, Red Bull,…
Paths
  LA to NY low-delay path for Cola
  Path may be non-shortest using RSVP-TE and SR-TE

## Slide 11: Service Creation

## Slide 12: Diverse Path Creation Example

## Slide 13: 3. Proactive Service Restoration
Optical interface cards generate heat and eventually fail
The CRC error rate increases as the card degrades
  This behavior can be learned
Service provider wants to proactively reroute critical services away from degrading equipment

## Slide 14: Self-Driving Network Trial
Performance Explorer detects link errors
  Orchestrator is notified
Orchestrator requests new paths for critical services
  New policy: “Exclude the problem link”
Path Provisioning application re-computes new paths avoiding the problem links
Orchestrator reconfigures routers

## Slide 15: Role of Machine Learning
CRC error rates are baselined for anomaly detection
  Need to be careful as there are no CRC errors when idle
The growth in CRC error rate can be detected
  Normalization
Why not use a neural network here?
  Really good match for the problem

## Slide 16: Neural Networks
Input layer
  The pixel values of the image
Hidden layers
Output layer
  Probability of a heart attack
  Age of the person
  BMI
  Smoker or not
  Whether has high blood pressure
Training data set: 300,000 retinal images and expected outputs
  Coefficients are determined by best-matching the training set
Test data set: 13,600 retinal images and expected outputs
  70% accurately predicted
  72% is the medical accuracy rate with a blood test
🏥

## Slide 17: Optical Interface Failure
Input layer: 5-minute CRC error rate for the last 30 days
Output layer: probability of a failure in next 1 hour, 1 day, 1 week, 1 month
Hidden layers: start with 2 layers and check the results if more needed
Training data set
Test data set
CRC Errors
Link Availability

## Slide 18: 1980s All Over Again
Algorithm – yes
Access to compute power – yes
Large data sets – not yet
  In the dataset:
    48 link failures over the week
    12 links
    Only one link stayed down for more than one hour
    9 interfaces with significant CRC errors, including this link

## Slide 19: 4. On-demand Traffic Engineering
Congestion caused by fiber cuts
  Normally the network is run uncongested
Traditional optimization algorithms are too slow
  NP-Complete
  Take hours to compute
Packet Design congestion-avoidance algorithm runs in seconds
  Polynomial time

## Slide 20: SDN Traffic Engineering Application
Topologies
Real-time physical or virtual
Link delay/loss/jitter
Baselines
Anomalies
Alerts
Traffic Matrices
Service aware
Peak or current traffic levels
Full-mesh or tactical
  Network Policies
  Under-/over-provision
  Optimization criteria
  Resiliency requirements
  Etc.
Policies
  TE Recommendations
  Add, delete, merge, split tunnels
  Programming
  SDN controllers
  Orchestrators
Physical & Virtual Routers, Switches & Network functions
Closed loop: analytics & policy-based recommendations, provisioning, monitoring
Notes: The Explorer SDN Platform enables closed loop analytics and automation to create more agile networks. Instead of requiring offline planning that can take hours or days, the SDN Platform computes in seconds the optimum traffic engineering configurations to achieve desired goals.

## Slide 21: Traffic Demands and Network Conditions

## Slide 22: TE Saves 60% Capacity

## Slide 23: 5. On-Demand Multi-Layer Traffic Engineering
Traffic engineering at the IP/MPLS layer
  IP rerouting is faster than optical – in sub-seconds
  Optimization algorithm must work in seconds also, not hours
Optimizing at the IP/MPLS layer alone may not always succeed
  Especially with fiber cuts
Optical network is slow but can help
  Capacity of some optical paths can be adjusted
    Flex-Ethernet, liquid-spectrum, partial restoration at the optical layer
  New optical transport paths can be signaled
Optical
IP/MPLS
Transitional links

## Slide 24: IP/MPLS and Optical Topology Correlation
Optical Service Path for an IP Link

## Slide 25: Multi-Layer Traffic Engineering
It is possible to re-engineer the IP links/ports and optical service paths
  However, optical rerouting is destructive and takes ~5 minutes
Re-engineer unused ports
  Ports of the failed links are unused
  Look for under-utilized link aggregation groups (LAGs)
Create new IP links between these ports
  Only where capacity is needed
  Coordinate IP and optical network changes to avoid packet drops

## Slide 26: Multi-Layer Traffic Engineering
Role of IP layer
  Identify the new layer 3 path
  Identify how much capacity is needed and where
Role of optical layer
  Repurpose an optical port on ROADM
  Signal two new paths
Role of orchestrator
  Coordinate the two pieces
  Add new IP links to the LAGs
3
1
4
2
3
1
4
2

## Slide 27: Role of Machine Learning
Many traffic patterns can be learned
  Traffic matrices with neural networks
    http://ieeexplore.ieee.org/document/7849067/
    https://arxiv.org/pdf/1711.02833.pdf
  DDoS
  Traffic anomaly detection
  Peering traffic optimization
  …

## Slide 28: BGP Route Hijacking
Happens too often
  BGP makes you (in)famous
Until we can protect the routing system, we need automatic detection and fast restoration
Baselining BGP routes helps

## Slide 29: BGP Route Baselines
Baselines
  Origin AS
  Neighbor AS
  2nd hop AS
  BGP next hop
Alerting

## Slide 30: Concluding Remarks
Network analytics empower many service provider use cases
Network trends and anomalies can be machine learned; some failures can be predicted
Self-driving network can reroute around congestion and move critical services away from failing equipment
Correlating IP and optical layers provides a more holistic self-driving network