## Slide 1: Link State Vector Routing
ENOG-16 2019
June 3rd 2019
Keyur Patel, CTO & Founder, Arrcus Inc.

## Slide 2: Agenda
Background and Motivation
LSVR Solution
LSVR Benefits & Takeaways

## Slide 3: Modern Data Centers
IP CLOS - Leaf-Spine fabric
Layer3 - BGP Routing Protocol (“Use BGP for Routing in Large-Scale Data Centers” in RTGWG)
Goals - Scale, Simplicity, Resiliency
What’s next
  Growing ECMP scale
  Increasing CLOS tiers
  New applications
EBGP
IP CLOS Fabric
Leaf
Spine

## Slide 4: BGP CLOS Architecture - Attributes
EBGP
IP CLOS Fabric
Leaf
Spine
Multiple Tiers
BGP Hop by Hop Peering
BGP configuration has direct co-relation with ECMPs – configuration explosion
Propagation of routing table to each hop
BFD for link level liveness

## Slide 5: CLOS IP fabric - Routing protocol comparison
Complete fabric topology at each node => Path computations – SPF, TE, CSPF, LFA; etc
Faster convergence
Simplicity – operational, troubleshooting (BRIB vs LSDB)
Incremental updates, no flooding and selective filtering
Reliable transport
Per-hop TE (UCMP)
Flooding of link-state
Complexity - State machine, LSDB
Convergence (per prefix, best path computation at every hop prior to advertisement)
Configuration
IGP
BGP

## Slide 6: LSVR – combining the best attributes of BGP and IGP
Use BGP as base protocol
Add the best of IGP characteristics
Link State Vector Routing (LSVR)
+
Complete fabric topology at each node => Path computations – SPF, TE, CSPF, LFA; etc
Faster convergence
Simplicity – operational, troubleshooting (BRIB vs LSDB)
Incremental updates, no flooding and selective filtering
Reliable transport

## Slide 7: LSVR Solution - Highlights
IP CLOS Architecture
  Multiple Tiers
  BGP peering with Route Controllers (/RRs)
    Simplified protocol configuration
  BGP configuration has direct co-relation with number of controllers *not* ECMP
    Control Plane Flooding optimized
  Route Controllers (/RRs) merely reflecting route updates
    No head of line blocking for update announcements
  Switches performing SPF algorithm to create graphs
    Distributed computing
  Overlay AFI/SAFIs (EVPN) can follow the same model with a traditional BGP
  BFD for Link layer liveness
Enabling new DC applications – flexibility, control, scale

## Slide 8: LSVR Solution – Flexible operational models
Centralized path computation
Distributed path computation
Inline Route controller
Centralized out-of-path Route Controller (/RR) – topology and path computation
Simplified management, single point for policy enforcement, enhanced path computation (CSPF) for traffic engineering, ORR
Can be coupled with BGP-SR in underlay for SR-TE
Centralized out-of-path Route Controller (/RR) – topology
Simplified management, single point for policy enforcement
Network nodes (Leaf-Spine) – distributed path computation
All nodes have full topology
Loop-free Alternates (LFA) computation, Fast Convergence
Inline Route Controller (/RR) on Spine – topology
Network nodes (Leaf-Spine) – distributed path computation
Leverage compute cores on Spine
Notes: Centralized Route controller.- Link discovery/liveliness May be done using LSOE or LLDP
Controller hierarchy must provide redundancy; can be less than fully connected - Must not be dependent on SPF for connectivity

## Slide 9: LSVR Solution – Protocol Enhancements
Define a new SAFI
  NLRI format is exactly same as BGP LS Address Family to carry link state information
BGP MP Capability and BGP LS Node attribute to assure compatibility
Multiple peering models supported
BGP runs Dijkstra instead of Bestpath decision process

## Slide 10: LSVR Solution - Best-Path Changes
Next-Hop and Path attributes announced as part of RFC4271
BGP Decision Process Phases 1 and 2 replaced by SPF algorithm
Decision Process Phase 3 may be short-circuited since NLRI is unique per BGP speaker
Need to assure the most recent version of NLRI is always used and re-advertised
  Augmented with support of sequence numbers

## Slide 11: LSVR Solution - SPF
Starting with greatly simplified SPF with P2P only links in single area (i.e., SPT)
Will scale very well to many use cases
Could support computation of LFAs, Segment Routing SIDs, and other IGP features
  BGP-LS format includes necessary Link-State
Link-State AF is dual stack AF since both IPv4 and IPv6 addresses/prefixes advertised
  BGP-LS format also supports VPNs but SPF behavior not defined
  Work needed to define interaction with existing unicast Afs
    Matter of local implementation policy

## Slide 12: LSVR - Route Origination
Routes originated by redistribution
Discovered using a new Discovery protocol - Layer 3 Liveness and Discovery protocol (L3DL)
  Used to discover unique identities of port/link including IP, MAC, Label binding
  Discover each other’s unique endpoint identification
  Discover configuration information
  Has layer2 keepalive for session continuity
  Standards being developed in LSVR WG at IETF
  Open source software efforts going on

## Slide 13: LSVR Solution - Convergence Improvements
BGP Link NLRI attribute BGP SPF Status TLV added
  Signals link down event without immediately withdrawing Link NLRI
BGP Prefix NLRI attribute BGP SPF Status TLV added
  Signals Prefix down event
NLRI Implicit withdrawal delay
  Avoids problem of flooding path discrepancies causing unnecessary route flaps
  Specifically, avoids flap when on fastest flooding path fails and NLRI is implicitly withdrawn before being received on others
Link Liveness is done using BFD

## Slide 14: LSVR Benefits & Takeaways
Builds on top of existing BGP protocol
Enables faster scale and convergence in growing ECMP IP CLOS fabrics
Enables centralized Route Controller architectures
Enables Traffic Engineering of underlay paths
When combined with overlay multi-tenant fabric solution like EVPN, LSVR enables Automation, Programmability and Resiliency
Ability to discover enhance link capabilities when combined with L3DL – facilitates route origination as well

## Slide 15: Thank You!